EXHIBIT “A”

PROPOSED REVISION

Allegheny County Health Department Rules and Regulations

Article XXI, Air Pollution Control

§2106.06, Mon Valley Air Pollution Episode (new)

And a related change to §2105.50, Open Burning

(Note: Portions of this proposed revision may also be submitted to the Pennsylvania DEP and U.S. EPA as a revision to Allegheny County’s portion of the Pennsylvania State Implementation Plan for the Attainment and Maintenance of the National Ambient Air Quality Standards, under Revision Tracking No. 97.)

Proposed Article XXI Revision – Mon Valley Air Pollution Episode Regulation

Because §2106.06 is a proposed new section, all type is shown in regular font.

Because §2106.06 is a proposed new section, all type is shown in regular font.

….

§2106.06  MON VALLEY AIR POLLUTION EPISODE {effective }

a.	Applicability.  This section applies to the following sources located in one or more of the municipalities identified in Subsection d:

1.	All major and synthetic minor sources of PM2.5;

2.	All sources that have combined allowable emissions from all emission units of 6.5 tons or more per year of PM2.5; and

3.	All sources that have combined allowable emissions from all emission units of 10 tons or more per year of PM10.

b.	Air Quality Forecast.  For purposes of this Section, the Department shall rely on the air quality forecast provided by the Pennsylvania Department of Environmental Protection for determining Mon Valley Air Pollution Episodes.  The Director of the Allegheny County Health Department may approve a change in the air quality forecast provider or methodology.  The Department shall post on its Air Quality Program website any changes to the air quality forecast provider or methodology.

c. 	Mon Valley Air Pollution Episodes.  For purposes of this Section, the “Mon Valley PM2.5 threshold level” shall be the value of the primary 24-hour PM2.5 NAAQS.

1.	Mon Valley Air Pollution Watch. The Department shall issue a Mon Valley Air Pollution Watch if the Department has determined from an air quality forecast that for at least the next 24-hour period atmospheric conditions will exist which indicate that the 24-hour average ambient concentration of PM2.5 in one or more of the municipalities identified in Subsection d is forecasted to exceed the Mon Valley PM2.5 threshold level.

2.	Mon Valley Air Pollution Warning. The Department shall issue a Mon Valley Air Pollution Warning if during a rolling 24-hour averaging period, the Mon Valley PM2.5 threshold level is exceeded at an official monitoring station in the municipalities identified in Subsection d and the Department has determined atmospheric conditions will continue as described in Paragraph c.1.

d.	Mon Valley Air Pollution Episode Area.  This Section shall apply to the following municipalities: City of Clairton, City of Duquesne, City of McKeesport, Borough of Braddock, Borough of Braddock Hills, Borough of Chalfant, Borough of Dravosburg, Borough of East McKeesport, Borough of East Pittsburgh, Borough of Elizabeth, Borough of Forest Hills, Borough of Glassport, Borough of Jefferson Hills, Borough of Liberty, Borough of Lincoln, Borough of Munhall, Borough of North Braddock, Borough of Port Vue, Borough of Rankin, Borough of Swissvale, Borough of Turtle Creek, Borough of Versailles, Borough of Wall, Borough of West Elizabeth, Borough of West Mifflin, Borough of White Oak, Borough of Wilmerding, Borough of Whitaker, Elizabeth Township, Forward Township, North Versailles Township, and Wilkins Township.

e.	Mon Valley Air Pollution Mitigation Plan.  In addition to any applicable plan requirements under Sections 2106.02 and 2106.05, all sources subject to this Section shall submit to the Department according to the schedule provided in Subsection f, a Mon Valley Air Pollution Mitigation Plan (referred to in this Section as “Plan”) with the following two phases:

1.	Mon Valley Air Pollution Watch Phase: A Mon Valley Air Pollution Watch Phase shall include procedures to ensure the source is operating in a manner consistent with good engineering practice and all air pollution control equipment is maintained in good working condition.  The Mon Valley Air Pollution Watch Phase  shall include procedures for record keeping and reporting to the Department the actions taken during the Mon Valley Air Pollution Watch period.  The Mon Valley Air Pollution Watch Phase  shall also include procedures to ensure that the source has sufficient staff and resources available to implement the Mon Valley Air Pollution Warning Phase within 24 hours of the Department’s notification to the source of a Mon Valley Air Pollution Watch.

2.	Mon Valley Air Pollution Warning Phase: A Mon Valley Air Pollution Warning Phase  shall include measures to reduce PM2.5 and PM10 emissions to minimize the impact on public health, safety, or welfare, the timeframe for implementing each measure, and an estimate of the PM2.5 and PM10 emissions reductions during a 24-hour period for each measure.  The Mon Valley Air Pollution Warning Phase  shall include the procedures identified in the Mon Valley Air Pollution Watch Phase and  procedures for record keeping and reporting to the Department the actions taken during the Mon Valley Air Pollution Warning period.  The measures to reduce PM2.5 and PM10 emissions may include, but are not limited to, the following:

A.	Reduce transportation activity;

B.	Switch or decrease fuel use as allowed by the facility’s permit issued under this Article;

C.	Delay nonessential activities that may cause emissions;

D.	Modify work or other practices; and

E.	Reduce, modify, cease, curtail, defer or postpone production and allied operations.

f. 	Dates for Submission of Mon Valley Air Pollution Mitigation Plan.  Sources subject to this Section shall submit the Mon Valley Air Pollution Mitigation Plan according to the following schedule:

1.  	Existing sources shall submit to the Department the Plan within 90 days after the effective date of this Section.

2. 	Sources that startup after the effective date of this Section shall submit to the Department the Plan within 90 days after initial startup of the source.

3.	Existing sources that become subject to this Section after the effective date of this Section shall submit to the Department the Plan within 90 days after the source becomes subject to this Section.

4.	Any person responsible for operation of the source shall advise the Department in writing of any change affecting the technical content or the implementation of the Plan no more than 30 days following the change.  Such submittals shall be reviewed and implemented according to the procedures described in Subsection g below.

g.	Procedure for Review and Effective Date of the Mon Valley Air Pollution Mitigation Plans.

1.	The Mon Valley Air Pollution Mitigation Plan shall be effective upon submission to the Department.

2.	If the Mon Valley Air Pollution Mitigation Plan is not acceptable to the Department, the Department shall issue an order directing the responsible person to modify and resubmit the Plan within thirty (30) days after receiving notice.  The order shall specify the reason or reasons for disapproval and shall specify the changes or additions necessary to make the Plan acceptable to the Department.  The Plan submitted for review to the Department under Paragraph g.1 shall continue to be effective until a modified Plan has been submitted.  The modified Plan shall be effective upon submission to the Department.

3.	When determining whether the Mon Valley Air Pollution Mitigation Plan is acceptable, the Department may consider the following factors:

a. 	The feasibility of implementing the Mon Valley Air Pollution Warning Phase within 24 hours of the Department’s notification to the source of a Mon Valley Air Pollution Watch;

b. 	Whether the measures to decrease PM2.5 and PM10 emissions can reasonably improve public health, safety, or welfare; and

c.	Whether the estimated reduction in PM2.5 and PM10 emissions is proportionate to the source’s contribution to emissions in any of the municipalities identified in Subsection d.

4.	In the event that a source fails to submit the Mon Valley Air Pollution Mitigation Plan according to the schedule provided in Subsection f, fails to resubmit the Plan, or fails to resubmit the Plan in accordance with the changes or additions specified by the Department, the Department, in addition to any other remedies available to it under this Article, shall have the authority to issue an order to that person detailing the procedures for a Mon Valley Air Pollution Watch or Warning Phase.

h.	Notification of Mon Valley Air Pollution Episodes. When a Mon Valley Air Pollution Watch or Warning is issued, the Department shall make the following notifications:

1.	The Department shall notify all sources subject to this Section that they are required to implement the procedures and measures identified in either the Mon Valley Air Pollution Watch or Warning Phase.

2. 	The Department shall notify all municipalities identified in Subsection d, and any other municipality that requests to be notified, that a Mon Valley Air Pollution Watch or Warning is in effect.

3. 	The Department shall issue an advisory on its Air Quality Program website and notify various media that a Mon Valley Air Pollution Watch or Warning is in effect.

i.	Termination of Mon Valley Air Pollution Episodes.

1.	The Department shall terminate any Mon Valley Air Pollution Watch or Warning when the conditions in Paragraphs c.1 and c.2 no longer exist.

2.	The Department shall issue a notification to all person(s) identified under Subsection h when the ACHD has determined that a Mon Valley Air Pollution Watch or Warning is no longer in effect.

j.	Other powers unaffected.  Nothing contained in this Section shall affect the power of the Department to issue an Emergency Order pursuant to §2109.05 of this Article, whether or not such emergency occurs during a Mon Valley Air Pollution episode.

For the following section:

Additions are shown in larger font, bolded, and underlined.

For the following section:

Additions are shown in larger font, bolded, and underlined.

§2105.50  OPEN BURNING  {Subsection f amended May 8, 2007, effective, August 17, 2007, and amended July 16, 2009, effective July 26, 2009.  Subsections a, b, and d amended, and e & f renumbered November 13, 2014, effective, January 1, 2015.  Paragraph a.3 amended mm/dd/yyyy, effective mm/dd/yyyy.}

a. 	General.

. . .

3. 	Wood burning activities shall not be conducted on Air Quality Action Days or in the municipalities identified in Subsection 2106.06.d when a Mon Valley Air Pollution Watch or Warning under Section 2106.06 has been issued, with the exception of conducting such burning for the commercial preparation of food.

____________________________________________________________________________________

End of Regulation Changes