EXHIBIT “A”

PROPOSED REVISION

Allegheny County Health Department

Rules and Regulations

Article XXI, Air Pollution Control

Part E, Subpart 9, §2105.90, “Source Emission and Operating Standards- Transportation Sources-Gasoline Volatility,”

And

Part G, §2107.15, “Methods-Gasoline Volatility and RFG;”

(This proposed revision will also be submitted to the Pennsylvania DEP and U.S. EPA as a revision to Allegheny County’s portion of the Pennsylvania State Implementation Plan for the Attainment and Maintenance of the National Ambient Air Quality Standards. Revision Tracking No. 89.)

- Proposed Gasoline Volatility Regulations Revisions

Deletions are shown with strikethroughs.

Additions are shown in larger font, bolded, and underlined.

PART E- Source Emission and Operating Standards

….

§2105.90 GASOLINE VOLATILITY

{This section added by May 7, 1998 amendment, effective May 15, 1998; Paragraph e renumbered, paragraphs c & d renumbered and amended August 12, 1999, effective September 1, 1999. Paragraph b.3 added mm/dd/2018, effective mm/dd/2018.}

a.	Applicability. This Section applies to gasoline which is sold or transferred into or within Allegheny County during the period May 1 through September 15, 1998, and continuing during the same period every year thereafter.

b.	Compliant Fuel Requirements.

1.	No refiner, importer, distributor, reseller, or carrier may:

A.. 	Sell, exchange or supply gasoline that is not a compliant fuel during the period described in Subsection (a).

B.	Blend, mix, store or transport or allow blending, mixing, storing or transporting of compliant fuel with noncompliant fuel during the period described in Subsection (a).

2.	No retailer or wholesale purchaser-consumer may sell, exchange, or supply gasoline that is not a compliant fuel during the period June 1 through September 15, 1998, and continuing during the same period every year thereafter.

3.	This Section will no longer be applicable upon the effective date of approval by the EPA of the removal, suspension or replacement of this Section as part of Allegheny County’s portion of the Pennsylvania SIP.

c.	Record keeping and reporting.

1.	Beginning with the terminal owner or operator who sells or transfers gasoline intended for use in Allegheny County during the period described in §2105.90(a), each time the physical custody of or title to a shipment of gasoline changes hands other than when gasoline is sold or transferred for use in motor vehicles at a retail outlet or wholesale purchaser-consumer’s facility, the transferor shall provide to the transferee a copy of the record described in this subsection.  Said record shall legibly and conspicuously contain, at a minimum, the following information:

(A)	The date of the sale or transfer.

(B)	The name and address of the transferor.

(C)	The name and address of the transferee.

(D)	The location of the gasoline at the time of transfer.

(E)	The volume of gasoline which is being sold or transferred.

(F)	A statement or grade code certifying that the gasoline has an RVP of 7.8 pounds per square inch or less per gallon.

2.	Any person who transports, stores, or sells compliant fuel that is intended for use in Allegheny County during the period described in §2105.90(a) shall segregate the compliant fuel from noncompliant fuel and the documentation described in §2105.90.c(1) shall accompany the compliant fuel at all times.

3.	Each person in the gasoline distribution network shall maintain records containing the compliance information listed in §2105.90.c(1).  These records shall be retained for at least 2 years from the date of the sale or transfer of compliant fuel. All records shall be kept on-site at each point in the distribution network, except for retail outlets. Retail outlets shall retain records on-site for at least the current compliance period (June 1 through September 15). The remaining records may be kept off-site, but they must be made available to the Department within 48 hours upon request.

d.	Labeling. During the period from June 1 to September 15 each year, and at all times when dispensing of clean fuels is required under this section, all retail gasoline dispensing facilities shall prominently display on each gasoline pump a label with the following statements and conditions:

1.	“Cleaner Gas”, and “JUNE 1 - SEPT 15".

2.	“RVP”.

3.	The letters “RVP” shall be a minimum of 5/16 inches in height; all other letters and numbers shall be a minimum of 1/4 inches in height.

4.	The letters “RVP” shall be printed in green and all the other letters shall be printed in black. The label background shall be white.

e.	Sampling and test methods.  Sampling and testing for the volatility of gasoline shall be performed according to the applicable procedures established §2107.15.

PART G - Methods

….

§2107.15 GASOLINE VOLATILITY and RFG

{This section added by May 7, 1998 amendment, effective May 15, 1998.

Subsection c added mm/dd/2018, effective mm/dd/2018}

a.	Volatility. Any sampling or testing of gasoline required by Section 2105.90 shall be performed according to the following methods as specified in Chapter 61 of the Allegheny County Source Testing Manual:

1.	Sampling of gasoline for the purpose of determining compliance with §2105.90 shall be conducted in accordance with 40 CFR Part 80, Appendix D (relating to sampling procedures for fuel volatility).

2.	Testing of gasoline for purposes of determining compliance with §2105.90 shall be conducted in accordance with 40 CFR Part 80, Appendix E (relating to test for determining the RVP of gasoline and gasoline-oxygenate blend).

b.	RFG. RFG shall be certified and tested in accordance with the requirements listed in 40 CFR Part 80 Subpart D (relating to reformulated gasoline) as specified in Chapter 61 of the Allegheny County Source Testing Manual.

c.	This Section will no longer be applicable upon the effective date of approval by the EPA of the removal, suspension or replacement of this Section as part of Allegheny County’s portion of the Pennsylvania SIP.

End of Regulation Changes